## Slide 1: Lab 1 Introduction
MMLAB

## Slide 2: Environment
Install Linux OS in a computer(VirtualBox or Vmware)
Ubuntu Server or Ubuntu Desktop is fine.
Using winsock for Windows Platform.

## Slide 3: Socket programming

## Slide 4: Socket
These two process should be different computer
Using IP + port + protocol to describe a communication

## Slide 5: OSI model
socket

## Slide 6: TCP
Transmission Control Protocol
Reliable(Three-way handshake)
In-order
Retransmission
Deprecate duplicated packets
congestion control/ flow control

## Slide 7: TCP flow
Establish socket
Bind address and socket
Designate socket
Waiting client…
Read socket
Write socket
Close socket

## Slide 8: Using System Call
int socket(int domain , int type, int protocal)
  Domain :
  type :
  Protocol :設定socket的協定標準，一般來說都會設為0，讓kernel選擇type對應的默認協議。
AF_UNIX/AF_LOCAL
AF_INET , AF_INET6
SOCK_STREAM：TCP。
SOCK_DGRAM：UDP
Notes: man socket

## Slide 9: 從Client連向Server
  IP and Port
  netinet/in.h已經為我們定義好了一個struct sockaddr_in來儲存這些資訊
  Ex :
  struct sockaddr_in {
  short sin_family; // AF_INET
  unsigned short sin_port; // port No
  struct in_addr sin_addr; // struct in_addr
  char sin_zero[8]; // Not used, must be zero */
  };
  struct in_addr {
  unsigned long s_addr; // load with inet_pton()
  };
Notes: man socket

## Slide 10: Using System Call
int connect(int sd , struct sockaddr *server, int addr_len)
  sd : socket的描述符
  server :負責提供關於這個socket的所有信息
  Ex :
  struct sockaddr_in info;
  bzero(&info,sizeof(info));//初始化
  info.sin_family = PF_INET;//sockaddr_in為Ipv4結構
  info.sin_addr.s_addr = inet_addr("123.123.13.12");//IP address
  info.sin_port = htons(8080);
addr_len : *server的大小
成功了就回傳0，不然就回傳-1
Notes: man socket

## Slide 11: Using System Call
ssize_t recv(int sockfd, void *buf, size_t len, int flags);
  Sockfd : socket的描述符
  buf : 讓Socket能把接收到的資料塞進裡頭
  Len : buf的大小
  Flags :接收的相關細節, Ex : blocking/nonblocking與超額接收等等
Notes: man socket

## Slide 12: Using System Call
  Return Value :回傳接收到了多少個位元組，若在接收時發生的錯誤則會傳回-1
  回傳0 :
    0 bytes
    兩方Socket設定的domain不一致
    當一方在正常情況下結束連線
Notes: man socket

## Slide 13: Using System Call
ssize_t send(int sockfd, const void *buf, size_t len, int flags);
  Sockfd : socket的描述符
  buf : 讓Socket能把接收到的資料塞進裡頭
  Len : buf的大小
  Flags :接收的相關細節, Ex : blocking/nonblocking與超額接收等等
Notes: man socket

## Slide 14: Using System Call
  Return Value :回傳送出了多少個位元組，若在接收時發生的錯誤則會傳回-1
  回傳0 :
    0 bytes
    兩方Socket設定的domain不一致
    當一方在正常情況下結束連線
Notes: man socket

## Slide 15: Using System Call
int bind(int sockfd, struct sockaddr* addr, int addrlen);
  Sockfd : socket的描述符
  addr : 與connetc()的 server 的設定大同小異 (INADDR_ANY)
  Len : *addr的大小
  Return Value : 0表示綁定成功，-1則表失敗
Notes: man socket

## Slide 16: Using System Call
int listen(int sockfd, int backlog);
  Sockfd : socket的描述符
  backlog :規定最多能有幾個人能連入server
  Return Value : 0表示成功，-1則表失敗
Notes: man socket

## Slide 17: Using System Call
int accept(int sockfd, struct sockaddr addr, socklen_t addrlen);
  Sockfd : socket的描述符
  addr : 描述Socket資訊的結構(空)
  addrlen: addr的大小
  Return value :一個新的Socket描述符，如果失敗則傳回-1(INVALID_SOCKET)
Notes: man socket

## Slide 18
socket
bind
Listen & accept
read
write
socket
connect
write
read

## Slide 19: TCP demo
np/tcp/echo_once/server.c
gcc –o server server.c
./server.c 5566
np/tcp/echo_once/client.c
gcc –o client client.c
./client.c localhost 5566

## Slide 20: UDP
User Datagram Protocol
Unreliable and more fast
no guarantee of transferring data bits or packets in an arranged manner

## Slide 21: UDP Flow (connectionless)

## Slide 22: UDP demo
np/udp/echo/server.c
gcc –o server server.c
./server
np/udp/echo/client.c
gcc –o client client.c
./client

## Slide 23: UDP File Transfer: TFTP(1/6)

## Slide 24: UDP File Transfer: TFTP(2/6)

## Slide 25: UDP File Transfer: TFTP(3/6)

## Slide 26: UDP File Transfer: TFTP(4/6)

## Slide 27: UDP File Transfer: TFTP(5/6)

## Slide 28: UDP File Transfer: TFTP(6/6)
回ACK

## Slide 29: 輸入為以下形式
執行檔需有5個參數
依序為tcp或udp, 傳送端或接收端, port, host, 傳送檔案路徑
$ ./lab1_file_transfer tcp send <ip> <port> test_input.txt
$./lab1_file_transfer tcp recv <ip> <port>
$./lab1_file_transfer udp send <ip> <port> test_input.txt
$./lab1_file_transfer udp recv <ip> <port>

## Slide 30: 報告內容包含
傳送Log, 每5%記錄一筆，需要紀錄傳送進度和時間
UDP版本的Packet Loss Rate
簡述UDP和TCP的差異在200字以內
200字的心得

## Slide 31: Lab1要求
1-to-1 UDP和TCP版本File Transfer的功能
程式可以傳送也可以接收資料(可從input控制是要傳還是要送)
能傳送1MB, 10MB, 100MB的測資，且不能把東西送壞掉
紀錄下傳送的LOG 每5% 記錄一筆
  例如
  5% 2018/03/20 12:00:20
  10% 2018/03/20 12:02:32
UDP版本需記錄下Packet Loss Rate (遺失封包/總傳送封包 x 100%)
心得200字

## Slide 32: Lab1作業繳交資訊
Moodle 上傳作業
報告請用PDF檔，code請用.c或.cpp檔，總共需要上傳兩個檔案
將兩個檔案壓縮, 檔名用自己的學號加上編號命名
  例如 P76031292_lab2_v1.zip
DUE : 2018. 4. 9(一) 23:59
TA mail :wucy@locust.csie.ncku.edu.tw